## Slide 1
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current flowing through a coil created by an external magnetic field

## Slide 2
USA Standards Correlation
FRAMEWORK FOR K-12 SCIENCE EDUCATION © 2012
The Dimension I practices listed below are called out as bold words throughout the activity.
Dimension 1 Science and Engineering Practices | ü | Asking questions (for science) and defining problems (for engineering) | ü | Use mathematics and computational thinking
 | ü | Developing and using models | ü | Constructing explanations (for science) and designing solutions (for engineering)
 | ü | Planning and carrying out investigations | ü | Engaging in argument from evidence
 | ü | Analyzing and interpreting data | ü | Obtaining, evaluating, and communicating information
Dimension 2 Cross Cutting Concepts | ü | Patterns | ü | Energy and matter: Flows, cycles, and conservation
 | ü | Cause and effect: Mechanism and explanation | ü | Structure and function
 | ü | Scale, proportion, and quantity |  | Stability and change
 | ü | Systems and system models |  | 
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 3
Dimension 3 Core Concepts | Discipline | Core Idea Focus
 | Physical Science | PS4: Waves and Their Applications in Technologies for Information Transfer
 |  | PS4.B: Electromagnetic Radiation
NGSS Standards | Middle School Standards Covered | High School Standards Covered
 | MS.PS-WER: Waves and Electromagnetic Radiation | HS.PS-ER: Electromagnetic Radiation
USA Standards Correlation
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 4
NATIONAL SCIENCE EDUCATION STANDARDS © 2002
USA Standards Correlation
Content Standards (K-12) |  |  | 
ü | Systems, order, and organization | ü | Evolution and equilibrium
ü | Evidence, models, and explanation | ü | Form and Function
ü | Constancy, change, and measurement |  | 
Physical Science Standards Middle School |  | Physical Science Standards High School | 
ü | Properties and Changes of Properties in Matter | ü | Structure of Atoms
ü | Motions and Forces | ü | Structure and Properties of Matter
ü | Transfer of Energy |  | Chemical Reactions
 |  | ü | Motions and Forces
 |  |  | Conservation of Energy and Increase in Disorder
 |  |  | Interactions of Energy and Matter
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 5
LEARNING OBJECTIVES
Core Objectives (National Standards):
Develop the ability to refine ill-defined questions and direct to phenomena that can be described, explained, or predicted through scientific means.
Develop the ability to observe, measure accurately, identify and control variables.
Decide what evidence can be used to support or refute a hypothesis.
Gather, store, retrieve, and analyze data.
Become confident at communicating methods, instructions, observations and results with others.
Activity Objectives:
The purpose of this activity is to study the relationship between an electric current inside a conductor and an external magnetic field. The electric current will be measured by the Globisens Labdisc electric current sensor.
Time Requirement: 45 - 60 minutes
USA Standards Correlation
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 6
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
Objective
The purpose of this activity is to study the relationship between
an electric current inside a conductor and an external magnetic
field. The electric current will be measured by the Labdisc’s
electric current sensor.

## Slide 7
The aim of the introduction is to focus students on the lesson subject by
refreshing acquired knowledge and asking questions which encourage
research development. Key concepts from the theoretical framework applied
by the students during the lesson are taught.
Introduction and theory
Introduction
Magnetic fields and electric current are closely connected. We can use
an electric current flowing inside a motor coil to rotate the motor and
convert electricity into a mechanical rotation; while on the other hand in a
generator we rotate a coil inside a magnetic field to create electricity and
produce current that will flow from the generator coil.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 8
Introduction and theory
TRY THIS!
Carefully cut a fizzy drink can approximately 5 cm from the base to obtain a
small metal container. Place it on a deep plate full of water. Fix a large magnet
to the end of a rope. Spin the magnet over the center of the can without
touching the sides… What happens to the can?
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 9
Introduction and theory
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
What do you think the magnets on the inside of headphones or loudspeakers are
for? Explain
At the end of this class you will be able to answer following questions and investigate!
In what situations have you used magnets or experimented with magnetism?
Carry out the experiment activity with your class so that at the end you’ll be able to
answer the following question.
Can we induce an electric current using a magnet?

## Slide 10
Theoretical
In physics, electric current is a flow of charge through a given point of space, in
a specific time period. The point of space is determined by an arbitrary reference
point. Historically, electric current was first studied by investigating how electric
charge transfers between two objects. The object where charged using friction or
induction methods.
In 1800 the Italian, Alessandro Volta built the first electric battery. The Dane,
Christian Oersted, used Volta´s battery when he discovered by accident in 1820
that there is a relationship between electric current and magnetism. He observed
how the needle in a compass moved when it was close to a conductor cable where
electricity was passing through.
Introduction and theory
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 11
Introduction and theory
This accident moved him to write that “all electric current or flow of charge
causes a magnetic field around the path of the conductor, whose magnitude
is inversely proportional to the distance between the observer and the electric
current”. Furthermore, the effect of a magnetic field can be amplified and
transmitted through a ferromagnetic material (a material that can turn into a
magnet if it is exposed to a magnetic field). Some examples of ferromagnetic
elements are iron (Fe), cobalt (Co) and nickel (Ni).
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 12
Introduction and theory
The expression for a magnetic field B caused by an electric current is:
Where:
B = magnetic field
I = electric current
r = radial distance to the observer
= magnetic permeability in free space
Staring from previous discoveries, in 1831 the Englishman, Michael Faraday made
a new discovery. He found out that in the same way that charges in motion cause
an electric field, a variation in the magnetic field also induces a force on the free
charges inside a conductor. This force is called electromotive force or EMF, and
drives the electric current to pass through the conductor. Therefore, electric current
may be induced by the movement of a magnet in a certain time period.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 13
Introduction and theory
Two years later, the German, Heinrich Lenz proved that “electromotive force gives
rise to a flow of charges whose magnetic field opposes its original cause, i.e. it
opposes the original change in magnetic flux”. This may be expressed in Faraday’s
Law of Induction:
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 14
Introduction and theory
Where:
= electromotive force (EMF)
t = time
B = magnitude of the magnetic field
S = area of the surface where the magnetic flux passes through (defined by the
conductor wire)
= angle between the magnetic field and the surface normal to S
Faraday´s Law means that the electromotive force ( ) is proportional to the change
in magnetic flux in a given time period. The change of magnetic flux opposes the
direction of the original magnetic field.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 15
Introduction and theory
Now students are encouraged to raise a hypothesis which must be tested with an experiment.
What will happen inside a copper coil if you move a magnet relative to the coil?
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 16
Activity description
Students will make a copper coil by coiling up a copper wire in their hands. They will then move a magnet several times relative to the coil to prove the Faraday and Lenz Laws
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
Warning!
Move all electronic devices away from the magnet to prevent them from being
adversely affected by the magnetic field.
At the end of the class, students will build an electromagnet and observe how the magnetic field affects the orientation of a compass needle.

## Slide 17
Labdisc
Red and black banana to banana connector cables
Ten meters of 1 mm copper wire
A neodymium magnet with at least 4000 gauss
rating
Resources and materials
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 18
Using the Labdisc
To collect measurements with the electric current sensor, the Labdisc must be set
up by following these steps:
a. Using the Labdisc
Open the GlobiLab software and turn on the Labdisc.
Click the Bluetooth icon in the bottom right corner of the GlobiLab screen.
Select the Labdisc you are using currently. Once the Labdisc has been
recognized by the software the icon will change from a grey to blue color.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 19
Using the Labdisc
Click on the button to configure the Labdisc. Select the current sensor in
the “Logger Setup” window. Enter “100/sec” for the sampling rate and
“10000” for the number of samples.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 20
Using the Labdisc
Once you have finished the sensor configuration start measuring by clicking
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
Once you have finished measuring stop the Labdisc by clicking

## Slide 21
Experiment
The following steps explain how to perform the experiment:
Take the copper wire and coil it around your hand, leaving about 10 cm of wire at
both ends free. Make sure the wire doesn’t unwind by fixing it with masking tape.
Connect the banana to banana cable to the Labdisc and to the ends of the copper
wire as shown in the figure below.
In the GlobiLab software click the RUN icon and observe the graph build on the
screen.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 22
Experiment
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
Start measuring, move the magnet two times inside and outside the coil. For the
first time do it slowly, moving the magnet more quickly on the second time.
Stop measuring.

## Slide 23
Results and analysis
The following steps explain how to analyze the experiment results:
Observe the chart that appears on the screen once you have finished measuring.
Identify the section of the graph where variations in the electric current were
recorded. Once you have found them, press to select the two points on the
graph representing the beginning and end of the current pulses section.
Press and then press OK. The graph was trimmed to show only the
“interesting section” of the current pulses.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 24
Results and analysis
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
Fit the scale to observe the variations in electric current displayed. To do this register
the maximum and minimum vales using the button, and enter rounded values
in the “Set Range” window by right-clicking the y axis on the chart.
Press and write notes on the graph specifying when the magnet was inside and
outside the wire coil.

## Slide 25
Results and analysis
How would you explain the variations in electric current?
How do the results relate to your initial hypothesis? Explain.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 26
Results and analysis
What differences did you find between the electric current when the magnet
was moving inside the coil and the electric current when the magnet was moving outside the coil?
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
When did you observe a larger current pulse – when the magnet was moving
slowly or when it was moving faster? Explain.

## Slide 27
Results and analysis
The graph below should be similar to the one the students came up with.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 28
Conclusions
How does the magnetic field inside the coil relate to the current recorded in the
coil? Explain.
Students should identify that the electric current is proportional to the CHANGE in the
magnetic field. Thus when the magnet is moving fast in and out of the coil - the graph
registers a higher pulse compared to a slow magnet movement. When the magnet
doesn’t move, even when it is inside the coil creating a high magnetic field, there will be no electric current.
What does the negative and positive sign of the electric current mean?
Students should point out that the sign represents the electrons’ direction of flow and is independent of the current’s magnitude.
Following are some questions and answers which should be developed by the students in order to elaborate their conclusions.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 29
Conclusions
How is the sign of the current inside the copper wire related to the magnetic field of the magnet? Explain.
Students should explain that according to the Lenz Law the electric current in the coil is opposite to the magnetic field creating it. Thus from the above recorded graph, students can clearly observe that when we insert the magnet into the coil, increasing the magnetic field, the current will be negative. Similarly, when the magnet is pulled out of the coil (magnetic field is decreased) the current will be positive.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 30
Activities for further application
How would you explain the phenomenon observed during the first activity called “TRY THIS!”?
Students should infer that the motion of the fizzy drink can is caused because of the action of a magnetic field on the fixed charges of the metal. Therefore the metal will move in an opposite direction than the current induced by the magnetic flux.
The aim of this section is that the students can extrapolate the acquired knowledge during this class through the application of it in different contexts and situations. Furthermore, it is intended that students wonder and present possible explanations to the experimentally observed phenomena.
Further questions:
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 31
Activities for further application
How could you use the Faraday and Lenz Law to produce energy in a hydroelectric
power plant? If you aren´t familiar with the process, investigate it.
Students should point out that the Faraday and Lenz Law may be used in a hydroelectric power plant to produce energy because the movement of a magnet inside a copper coil (dynamo) induces electric current. Water that falls on sails produces a circular movement of the magnet.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field

## Slide 32
Activities for further application
Could you build an electromagnet with a copper wire, a battery and a piece of iron?
Try it using the materials of the experiment.
Students should deduce that if they coil the copper wire around the piece of iron
and connect the wire to a power supply, a magnetic field will appear. Since iron is a
ferromagnetic material, the magnetic field will amplify and reach a high magnitude,
depending on the electric current that passes through the conductor.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field
How do you think the orientation of a compass would be affected if you exposed it to an electromagnet? Prove your theory with the electromagnet you built to answer the previous question.
Students should point out that the compass orientates according to the north pole of the
natural magnetic field on our planet. If we expose the compass to a magnetic field
other than that of Earth, its orientation will change. We can prove this by coiling
a copper wire around a piece of iron and connecting the end to a battery. Next we
place the compass in front of the electromagnet and try connecting and disconnecting the wire to the battery. The orientation of the needle inside the compass will change depending on if it is orientated by the magnetic field of the planet or by the magnetic field of the electromagnet.

## Slide 33
Activities for further application
What will happen to the direction of the needle if you switch the cables connected to the battery?
Students should point out that the direction of the needle’s movement will change
due to the change in the battery’s polarity which then causes a change in the direction of the electric flow.
Electricity and magnetism
Verifying the Lenz Law by measuring the electric current
flowing through a coil created by an external magnetic field