## Slide 1
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 2
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Objective
The purpose of this activity is to relate light absorbance and transmittance in solutions with different concentrations, create a hypothesis and proceed to test it using the Labidsc colorimeter sensor.

## Slide 3
The aim of the introduction is to focus students on the lesson subject by refreshing acquired knowledge and asking questions which encourage research development. Key concepts from the theoretical framework, applied by the students during the lesson, are taught.
Introduction and theory
Introduction
As part of our everyday life we prepare and use different solutions. Each one is
composed of two parts: The solvent (most of the time water), i.e. the substance
into which the solute is dissolved; and the solute, which is the substance that is
dissolved in the solvent. A common example of a solution may be salt water for
cooking pasta, which becomes more salty the more concentrated the solution is.
When you are doing scientific work, particularly in chemistry, biology or medical
sciences, it is very important to know exactly the concentration of the solutions
you are working with. To measure concentration, several techniques can be used.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 4
Introduction and theory
Carry out the experiment activity with your class so that at the end you’ll be able to
answer the following question:
Can you think of some different solutions you have prepared at school or at home?
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
When you are making tea, how do you know when it is ready? Describe.
How can a light beam that passes through a sample of a given solution help determine
its concentration?

## Slide 5
Theoretical
A solution is a homogeneous mixture of two or more substances that exist in a single concentration. To determine the concentration of a given solution you can apply the Beer-Lambert law. This law states that the concentration of a solute is proportional to the absorbance.
The colorimeter allows light to pass through a cuvette containing a sample of the solution which absorbs some of the incoming beam. When the ray of light of a given wavelength and intensity I comes perpendicularly into contact with the solution of a tinted chemical compound, the compound will absorb part of the radiation (Ia). The remaining part of the solution (Ib) will strike a detector. As such the following equation is demonstrated:
Introduction and theory
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 6
Introduction and theory
The absorption of light is related to the number of molecules present in the solution
(concentration of the solution).
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 7
Introduction and theory
The Beer-Lambert law defines the relationship between the concentration of a solution and the amount of light absorbed by the solution:
Where:
A = Absorbance
= Molar absorptivity [L mol cm ]
d = Path length of the cuvette containing the sample [cm]
C = Concentration of the compound in solution [mol L ]
Transmittance is the relationship between the amount of light that is transmitted to the
detector once it has passed through the sample (I) and the original amount of light (I0). This is expressed in following formula:
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
-1
-1
-1

## Slide 8
Introduction and theory
Where I0 is the intensity of the incident light beam and I is the intensity of the light coming out of the sample. Transmittance is the relative percent of light passed through the sample. Thus, if half the light is transmitted, we can say that the solution has a 50% transmittance.
The relations between transmittance (T) and absorbance (A) can be expressed by following:
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 9
Introduction and theory
Now students are encouraged to raise a hypothesis which must be tested with
an experiment.
If you have one solution of different concentrations, how do you expect the
transmittance percentages to change when you measure from the lowest to
the highest concentration? Why?
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 10
Activity description
Students will study the relationship between transmittance, absorbance
and concentration of one solution using the Lambert-Beer law. They will
calculate the concentration of a sample using mathematical tools for
graph analysis.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 11
Activity description
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Preparation of the samples
The teacher will prepare two samples of solution for the students. The students will obtain the concentrations of the samples through the experiment.
The instructions to prepare the samples are as follows:
The teacher will give 3 mL. of one of the samples to each work group. The students will be told that they have to obtain the concentration. At the end of the class they will compare their results with the theoretical value.

## Slide 12
Activity description
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Students will read a graph to obtain the concentration. To understand it they have to know the slope-interception form for the equation of a line.
Y = mX + n
Where
m = slope
X = x coordinate
Y = y coordinate
n = y intercept (where the line crosses the y axis)
Students must:
1. Obtain the transmittance percentage by using the colorimeter.
2. Divide the transmittance percentage by 100 to obtain transmittance (T) of the sample.
3. Calculate absorbance (A) using the following formula: A = LOG10T.
4. Obtain X by solving the slope-interception equation, substituting the y coordinate for
the activity description absorbance value.

## Slide 13
Labdisc
Resources and materials
USB connector cable
Cuvette for the colorimeter
Distilled water
Paper towel
Instant coffee
100 mL beaker
4 test tubes
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Wash bottle
Stirrer bar
Balance

## Slide 14
Using the Labdisc
a. Labdisc Configuration
To collect measurements with the microphone sensor, the Labdisc must be set up according to the following steps:
Open the GlobiLab software and turn on the Labdisc.
Click on the Bluetooth icon in the bottom right corner of the GlobiLab screen. Select the
Labdisc you are using currently. Once the Labdisc has been recognized by the software,
the icon will change from a grey to blue color . If you prefer a USB connection follow the previous instruction clicking on the USB icon. You will see the same color change when the Labdisc is recognized .
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 15
Using the Labdisc
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Click on to configure the Labdisc. Select colorimeter in the “Logger Setup” window.
Enter “Manual” for the sample frequency and the number of samples.

## Slide 16
Using the Labdisc
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Once you have finished the sensor configuration start measuring by clicking .
Once you have finished measuring stop the Labdisc by clicking .

## Slide 17
Experiment
The following steps explain how to perform the experiment:
Mark each beaker with the number of the sample (1 to 6).
Place distilled water in beaker 1.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Note: Before you start recording, calibrate the colorimeter with the solvent you will
use during the experiment. This step is important to minimize the experimental error
of the measurement. To calibrate, add some solvent (in this case, distilled water),
filling ¾ of the sensor’s cuvette and place the cuvette in the output. Then, press the
button on the colorimeter until you hear the Labdisc’s signal. Once you have finished
the calibration remove the cuvette from the colorimeter.

## Slide 18
Experiment
Measure the transmittance of the solution. To take a data reading, fill the cuvette until it is ¾ full with solution from sample 1. ALWAYS hold the upper part of the cuvette to ensure the sides remain clean from fingerprints.
Prepare samples 2 to 6 as shown in the table below by measuring the amount of distilled water (solvent) and adding 1 gram of coffee (solute) to each glass.
Use the stirrer bar to mix the coffee until it dissolves completely.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Clean and dry the cuvette with paper towels.

## Slide 19
Experiment
Place the cuvette in the output of the colorimeter. Cover the cuvette moving the edge of the Labdisc and start measuring.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 20
Experiment
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Record the transmittance percentage. Take the sample out of the sensor and clean the cuvette with distilled water. Repeat the steps with the other samples.
Once you have finished measuring stop the Labdisc.

## Slide 21
Experiment
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
The graph below should be similar to the one the students came up with. The decreasing order of percentages can also be observed in both green and blue colorimeters.
Transmittance percentage as a function of concentration:

## Slide 22
Results and analysis
The following steps explain how to analyze the experiment results:
Export the data to Excel clicking on . Save the data on your computer.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Observe the percentage transmittance values obtained when we illuminate the samples with different light beam colors (different wavelengths: Red, green and blue).

## Slide 23
Results and analysis
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Organize the data and calculate transmittance and absorbance values starting from the
transmittance percentage given by the Labdisc. Data should be organized as shown in the
following table:
Sample – Concentration [gr/mL] - %Transmittance red – Transmittance red – Absorbance red - %Transmittance green – Transmittance green – Absorbance green - %Transmittance blue – Transmittance blue – Absorbance blue

## Slide 24
Results and analysis
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Label column C as percentage transmittance of red, column F as percentage transmittance of green and column I as percentage transmittance of blue. Use the formula of the table to calculate the transmittance (columns D, G and J) and absorbance (columns E, H and K) of each sample.
Observe and compare the transmittance values for each sample. Remember that the Lambert-
Beer law can be used for absorbance values between 0 and 1. Therefore, select the color where you
obtained most results within this absorbance range.
Create a line graph of absorbance as a function of concentration. To do this, first create a scatter
plot by clicking on the button.
Select the Data Range. Select the concentrations value for the x axis and absorbance values for the
y axis.
Add a regressing line to the graph by right-clicking on the points and selecting “Add Trendline”.
Select the linear regression type. Choose the options chart and select “Display equations on chart”.
Press Ok to finish.

## Slide 25
Results and analysis
What was the relationship between the transmittance and concentration of the
solutions?
How do the results relate to your initial hypothesis? Explain.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
What was the relationship between the absorbance and concentration of the
solutions?

## Slide 26
Results and analysis
The graph below should be similar to the one the students came up with.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations
Concentration as a function of absorbance: Y axis: Absorbance [red colorimeter]
X axis: Concentration [gr/mL]

## Slide 27
Conclusions
What variables are related in the Lambert-Beer law?
Students should point out that the Lambert-Beer law relates absorbance of a solution to its concentration.
Following are some questions and answers which should be developed by students in order to elaborate on their conclusions.
If you have a solution and samples of it with different concentrations; in which range of absorbance can we use the Lambert-Beer law?
Students should go over the information given in the theoretical framework and point out that the Lambert-Beer law is only valid for absorbance values between 0 and 1.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 28
Conclusions
Suppose the equation on the Excel graph of absorbance as a function of concentration is a straight line. What is the relationship between the expression and the variables related in the Lambert-Beer law?
Students should understand the meaning of the equation of the graph. In this case, the y
coordinate represent absorbance and the x coordinate concentration. Therefore, we can
understand the equation as following expression:
Absorbance = m * Concentration + n
If you have a sample of unknown concentration, how would the Lambert-Beer law
be useful?
Students should point out that you can obtain the concentration of an unknown sample by measuring
absorbance and using the Lambert-Beer´s law to compare its absorbance to a known solution as an
absorbance reference.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 29
Activities for further application
Suppose you have an instant coffee solution of an unknown concentration which you want to calculate using the Lambert-Beer law. However, your absorbance is higher than one - how can you calculate concentration?
Students should point out that they will have to decrease the absorbance value to use the Lambert-Beer law, diluting the initial sample to obtain an absorbance value between 0 and 1. Starting from that point, they could calculate the concentration of the diluted solution and then the concentration of the original sample.
The aim of this section is for students to extrapolate the acquired knowledge during this class through its application in different contexts and situations. Furthermore, it is intended that students question and present possible explanations to the experimentally observed phenomena.
Further questions:
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations

## Slide 30
Activities for further application
What was the concentration of the sample prepared by your teacher?
Students should use the knowledge obtained during the class to calculate the concentration of the work sample and obtain 0.0071 [gr/mL] or 0.011 [gr/mL] approximately, depending on the sample they worked with.
Concentrations that absorb
Measuring percentage transmittance of solutions at different concentrations